## Slide 1: ECE 322L Electronics 2
03/24/20- Lecture 16
AC load line
Maximum symmetrical swing

## Slide 2
Updates and overview
3/24/20
Midterm will be available on UNM Learn starting on Tue 03/31/2019, 10:30 am and it will be due on on Tue 03/31/2019 via upload to UNM Learn at 12:30 pm.
Focus: DC and AC analysis of the BJT.
See the practice problems on UNM Learn to get
a better idea of the format.
We will be going to the frequency response of amplifiers next (Neamen Ch. 7).
A handout on Bode plots and simple transfer functions is on UNM Learn (please, study/review before Lecture 17).
Today: AC load line, compliance, and maximum symmetrical swing (Neamen 6.5.2, notes and handouts on UNM Learn).

## Slide 3: Compliance
Compliance of a voltage amplifier:
Maximum possible output voltage swing for a given amplifier
3/24/20
When the output voltage exceeds the compliance of the amplifier a part of the signal will be clipped and distortion will occur.
Note: The definition can be applied to any current or voltage in the circuit.
Notes: This slides provides the definition of compliance for a voltage amplifier

## Slide 4: Compliance vs Max. Symm. Swing
3/24/20
Compliance of a voltage amplifier:
Maximum possible output voltage swing for a given amplifier
Maximum symmetrical swing of a voltage amplifier
Maximum peak-to-peak value of the output voltage that is symmetrical around the its DC value.
Notes: This slides specifies the difference between compliance and maximum symmetrical swing. The compliance of a signal is not necessarily symmetrical around its DC value. The compliance of a voltage signal is just the maximum possible voltage swing for that signal. The next two slides will specify the phenomena that limit compliance in a BJT based voltage amplifier.

## Slide 5: Origin of clipping-Saturation clipping
Clipping occurs because the transistor is no longer in active region, and it goes in cut-off or saturation.
3/24/20
At low vCE The compliance is limited by the BJT entering saturation
More prone to occurring
when the Q point is
close to saturation
Notes: The compliance of a BJT based voltage amplifier is limited by the BJT going out of the forward active region and into out saturation or cut-off. This slides shows a case where the maximum swing or compliance is limited by the BJT going in saturation. The plot shows the ac load line or the load line of the ac circuit of the amplifier. (In a few slides I will show you how to sketch the load line and how to use it to determine the compliance of a voltage amplifier) The Q point is also marked on the ac load line. Note that the Q is closer to the saturation region than to the cut-off region in this case. The plot also show how the iC and vCE vary as the input signal varies. In other words the Q points moves up and down the ac load line as the input signal oscillates. At vCE lower than vCE, sat~0.1-0.3 V the transistor goes into saturation and both the iC and the vCE are clipped.

## Slide 6: Origin of clipping-Cut-off clipping
Clipping occurs because the transistor is no longer in active region, and it goes in cut-off or saturation.
3/24/20
At high vCE compliance is limited by the BJT entering cut-off
More prone to occurring
when the Q point is
close to cut-off
Notes: This slides is limited by shows a situation where the compliance is limited by the transistor entering in cut-off as the input signal oscillates. This is the case of a Q point closer to the cut-off region than to the saturation region.

## Slide 7: Determine the maximum symmetrical swing
The ac load line is used to determine the maximum symmetrical swing (Vpp) for a given amplifier.
Note that the ac load-line can also be used to determine the compliance of the amplifier.
3/24/20

## Slide 8
R1, R2 Þ set the value of VB , IB at a given VCC
RE Þ stabilizes the Q point
RL Þ Load
DC and AC load lines
3/24/20
Notes: We are now going to consider this common emitter amplifier to understand how to sketch the ac load line and what kind of information the ac load-line provides.

## Slide 9
Complete Circuit
DC circuit
AC circuit
DC and AC circuits
3/24/20
Notes: This slides shows the total circuit for the CE amplifier (left), the DC circuit (middle) and the AC circuit (right) in the midband.

## Slide 10
DC load line (Output)
We obtain the DC load line by writing a KVL on the C-E loop (output)
3/24/20
Notes: This slides illustrates the process to obtain the equation of the DC load line and shows the DC load line.

## Slide 11
The DC load line is determined by the VCC, RC and RE.
The collector current IC and the collector-emitter voltage VCE must lay on the DC load line.
The intersection of the transistor characteristics at the DC bias value of IBQ with the DC load line determines the Q-point.
DC load line (Output)
The dc load line represents all the possible combinations of IC and VCE for a given amplifier
3/24/20
Notes: This slides summarizes important facts about the DC load line

## Slide 12
DC biasing and AC signal
3/24/20
The DC load line does not describe how the Q point changes in response to an applied ac input signal because dc and ac circuits have a different layouts, which yields different load lines.
Complete Circuit
DC circuit
AC circuit
Notes: This slides explains why the DC load line doesn’t describe the variation of the Q point in response to an applied ac signal.

## Slide 13: AC Load line
Equation of the ac load line
The AC load line can be sketched or plotted in the DC+AC plane just like the DC load line (see handout).
3/24/20
Notes: This slides shows how to sketch the ac load line. The first step is to sketch the ac circuit. The second step is to write a KVL at the output loop. The KVL will yield the equation of the ac load line. Note that the ac load line will relate ic (ac signal) to vce (ac signal). The third step is to determine the intercept of the ac load lines with the iC and vCE axis. The fourth step is to sketch the ac load line in the DC+AC space (iC-vCE). Please, see additional notes on this in lecture 16 folder.

## Slide 14: DC and AC Load Lines
The DC and the AC load lines
differ due to different layouts in DC and AC
3/24/20
Notes: This slides compares the DC and AC load-lines. Typically the AC load line has higher slope than the DC load line as its slope is inversely proportional to the load resistance, which is small.

## Slide 15: Compliance and AC load line
Compliance is determined by calculating the maximum range of output voltage (DC+AC) before the transistor enters cut-off and saturation.
The compliance of a voltage amplifier is determined using the concept of AC load line.
3/24/20
Notes: The next few slides will show how to utilize the ac load line to calculate the compliance of the amplifier. As stated previously, the compliance is limited by the transistor entering saturation or cut-off. We will then determine some useful conditions for the transistor to enter saturation and cut-off based on the ac load line.

## Slide 16: Cut-off limit
3/24/20
Notes: This slides determines the limit posed on the vCE by the BJT going into cut-off. The plot shows the ac load line in the iC-vCE space. Assume the transistor is biased at a certain VCEQ. Now focus on the vCE axis. The maximum possible change of the vCE from the VCEQ before the transistor goes in cut-off is ICQrc . Twice this value will give the maximum peak to peak transition of the vCE.

## Slide 17: Saturation limit
3/24/20
Notes: This slides determines the limit posed on the vCE by the BJT going into saturation. The plot shows the ac load line in the iC-vCE space. Assume the transistor is biased at a certain VCEQ. Now focus on the vCE axis. The maximum possible change of the vCE from the VCEQ before the transistor goes in saturation is VCEQ . Twice this value will give the maximum peak to peak transition of the vCE.

## Slide 18: Compliance limits: summary
3/24/20
Notes: Thelim peak-to-peak value of the output voltage is limited to the ranges A and B when the transistor enters cut-off or saturation, respectively.

## Slide 19: Maximum symmetrical swing
3/24/20
Maximum peak-to-peak value of the output voltage which is symmetrical around the Q point.
Minimum between A and B
*Note that the absolute values of ICQ and VCEQ should be used to calculate compliance and maximum symmetrical swing.
Notes: In order to determine the maximum symmetrical swing of the output voltage one will have to determine the peak-to-peak limits imposed by to the voltage values by the transistor going in cut-off or saturation (Conditions A and B). This will require to determine the Q point and the slope of the ac load line. Then you will have to take the minimum value between the peak-to-peak voltages that you calculated using conditions A and B. Selecting the minimum value between the two will ensure that the swing is not only maximum but also symmetrical.

## Slide 20: Lecture 16, In class problem
3/24/20
Design a bias stable circuit such that the collector current is 1.6 mA.
Determine the maximum symmetrical swing for a load of 8 W and for a load of 5kW
*See solution in the handout within lecture 16 folder.

## Slide 21: Lecture 16, Take home problem
3/24/20
Note: Part a is the same as the in class problem.

## Slide 22: Overview of lecture 17
Amplifier gain vs frequency (Neamen 7.1)
Low-frequency response of an amplifier (Neamen 7.3)
Please, review the handout about simple transfer functions and Bode plots (Neamen 7.2) before Lecture 17
3/24/20