## Slide 1: Handout on compliance and ac load line
ECE 322L

## Slide 2: Cutoff and Saturation Clipping
When determining the output compliance for a given amplifier, solve both equation (A) and (B). The lower of the two results is the compliance of the amplifier.

## Slide 3: Compliance

## Slide 4: Compliance
The maximum possible transition for VCE is equal to the difference between VCE(off) and VCEQ. Since this transition is equal to ICQrC, the maximum peak output voltage from the amplifier is equal to ICQrC. Two times this value will give the maximum peak-to-peak transition of the output voltage:
VPP = the output compliance, in peak-to-peak voltage
ICQ = the quiescent value of IC
rC = the ac load resistance in the circuit
VPP = 2ICQrC
(A)

## Slide 5: Compliance
When IC = IC(sat)­, VCE is ideally equal to 0V. When I­C = ICQ, VCE is at VCEQ. Note that when IC makes its maximum possible transition (from ICQ to IC(sat)), the output voltage changes by an amount equal to VCEQ. Thus the maximum peak-to-peak transition would be equal to twice this value:
Equation (A) sets the limit in terms of VCE(off). If the value obtained by this equation is exceed, the output voltage will try to exceed VCE(off), which is not possible. This is called cutoff clipping, because the output voltage is clipped off at the value of VCE(off).
Equation (B) sets of the limit in terms of IC(sat). If the value obtained by this equation is exceed, the output will experience saturation clipping.
(B)
VPP = 2VCEQ