## Slide 1: ECE 530 Cloud Computing
Ioannis Papapanagiotou
Synchronous and Asynchronous Execution

## Slide 2: Synchronous and Asynchronous Executions
p
q
r
p
q
r
…processes share a synchronized clock
In the synchronous model messages arrive on time
… and failures are easily detected
None of these properties holds in an asynchronous model

## Slide 3: Reality: neither one
Real distributed systems aren’t synchronous
  Although a flight control computer can come close
Nor are they asynchronous
  Software often treats them as asynchronous
  In reality, clocks work well… so in practice we often use time cautiously and can even put limits on message delays
For our purposes we usually start with an asynchronous model
  Subsequently enrich it with sources of time when useful.
  We sometimes assume a “public key” system. This lets us sign or encrypt data where need arises

## Slide 4: Thought problem
Jill and Sam will meet for lunch. They’ll eat in the cafeteria unless both are sure that the weather is good
  Jill’s cubicle is inside, so Sam will send email
  Both have lots of meetings, and might not read email. So she’ll acknowledge his message.
  They’ll meet inside if one or the other is away from their desk and misses the email.
Sam sees sun. Sends email. Jill acks’s. Can they meet outside?

## Slide 5: Sam and Jill
Sam
Jill
Jill, the weather is beautiful! Let’s meet at the sandwich stand outside.
I can hardly wait. I haven’t seen the sun in weeks!

## Slide 6: They eat inside! Sam reasons:
“Jill sent an acknowledgement but doesn’t know if I read it
“If I didn’t get her acknowledgement I’ll assume she didn’t get my email
“In that case I’ll go to the cafeteria
“She’s uncertain, so she’ll meet me there

## Slide 7: Sam had better send an Ack
Sam
Jill
Jill, the weather is beautiful! Let’s meet at the sandwich stand outside.
I can hardly wait. I haven’t seen the sun in weeks!
Great! See yah…

## Slide 8: Why didn’t this help?
Jill got the ack… but she realizes that Sam won’t be sure she got it
Being unsure, he’s in the same state as before
So he’ll go to the cafeteria, being dull and logical. And so she meets him there.

## Slide 9: New and improved protocol
Jill sends an ack. Sam acks the ack. Jill acks the ack of the ack….
Suppose that noon arrives and Jill has sent her 117’th ack.
  Should she assume that lunch is outside in the sun, or inside in the cafeteria?

## Slide 10: How Sam and Jill’s romance ended
Jill, the weather is beautiful! Let’s meet at the sandwich stand outside.
I can hardly wait. I haven’t seen the sun in weeks!
Great! See yah…
Got that…
Maybe tomorrow?
Yup…
Oops, too late for lunch
. . .

## Slide 11: Things we just can’t do
We can’t detect failures in a trustworthy, consistent manner
We can’t reach a state of “common knowledge” concerning something not agreed upon in the first place
We can’t guarantee agreement on things (election of a leader, update to a replicated variable) in a way certain to tolerate failures

## Slide 12: Back to 2PC and 3PC
Summary of the state of the world?
  3PC would be better than 2PC in a perfect world
  In the real world, 3PC is more costly (extra round) but blocks just the same (inaccurate failure detection)
  Failure detection tools could genuinely help but the cloud trend is sort of in the opposite direction
  Cloud transactional standard requires an active, healthy logging service. If it goes down, the cloud xtn subsystem hangs until it restarts
We’ll be using both 2PC and 3PC as a building block but not necessarily to terminate transactions.

## Slide 13: Acknowledgements
CS5412 Spring 2012 (Cloud Computing: Birman)