## Slide 1: UART Interface
Dr. Edward Nava
ejnava@unm.edu

## Slide 2: PIC Architecture

## Slide 3: UART Block Diagram

## Slide 4: UART Interface
Characteristics
  Asynchronous
  Uses a minimum of two signal wires, Tx and Rx
  Can use two optional flow control signals, Request to Send (RTS) and Clear to Send (CTS)
  Full Duplex communication
  Supports multiple protocols and configurations
  Requires both Sender and Receiver configuration of data rates and protocol options.

## Slide 5: Communication Between Devices
When devices are transferring data between each other, they require:
  A protocol which defines how the data are to be extracted from the electrical signal.
  A means by which to determine the start and the end of the transmission.

## Slide 6: Asynchronous Communication Protocol Detail
For two UARTs to communicate with each other, both must be configured with identical values for:
  Bit Rate Clock
    Baud Rate
  Framing
    Start Bit
    Data Bits
    Parity (if used)
    Stop Bits

## Slide 7: UART Signals
For wired communications, the following signals are used:
  Tx – Transmit Data
  Rx – Receive Data
  CTS – Clear to Send (Optional for hardware handshake)
  RTS – Request to Sent (Optional for hardware handshake)
Note: The Tx line of one of the communicating devices must be tied to the Rx line of the other device and vice versa.

## Slide 8: Signal Interconnects
TX
TX
RX
RX
RTS
RTS
CTS
CTS
Optional
UART 1
UART 2

## Slide 9: UART Data Communication Protocol
When the communication link is idle, the transmit line is at a logical one level.
When a transmission is starting, the transmit line is lowered to a logical zero level and is held for one bit time. This is what is called the start bit.
Following the start bit, 8 or 9 data bits are transmitted.
If 8 data bits are being transmitted, an optional parity bit may be transmitted.
After the data and parity bits have been transmitted, the transmit line is raised to a logic one level for one or two bit times, indicating the end of the transmission. The end bit(s) are called the stop bit(s).

## Slide 10: Single Character Transmission
The transmission begins with a start bit, which is followed by 8 or 9 data bits, then possibly a parity bit, and ends with one or more stop bits

## Slide 11: Sequential Transmissions
With sequential transmissions, the start bit of the subsequent character(s) follows immediately after the prior transmission’s stop bit(s)

## Slide 12: Vintage Data Terminal

## Slide 13: RS-232
RS-232 is a standard for serial communication that specifies:
  Connectors
  Pin Assignments
  Voltage Levels
  Baud Rates
RS-232 uses a bipolar signal to represent logic values
  +3V to +12V – represents a logical 0
  -12V to -3V – represents a logical 1
Terminology
  DTE – Data Terminal Equipment (Like a terminal)
  DCE – Data-Circuit Terminating Equipment (Like a modem)

## Slide 14: PIC32 UARTs on MX7
The PIC32 microcontroller has six UARTs
Two UARTs are accessible on the MX-7 development board
On the MX-7 board, UART1 is connected to the USB serial converter – Using this UART can cause problems when using the MPIDE development system.
UART2 signals are accessible via connector JF

## Slide 15: UART SFRs

## Slide 16: UART2 Connection on MX7

## Slide 17: UART Crossover Cable

## Slide 18: Multi-Character Transmission