## Slide 1: ECE 322L Electronics 2
04/21/20 - Lecture 23
Class AB amplifiers

## Slide 2
Class AB amplifiers
  Definition and general architecture
  Voltage-transfer characteristic (VTC)
  Output resistance
  Biasing configurations
(Neamen 8.3.3 and from 8.5.1 to 8.5.4-S&S, 6th edition, 11.5)
Overview

## Slide 3
Class-A: Output device(s) conduct through 360 degrees of input cycle (never switch off).
Class-B: Output devices conduct for 180 degrees (1/2 of input cycle).
Class-AB: Halfway (or partway) between the above two examples (181 to 200 degrees typical).
Class-C: Output device(s) conduct for less than 180 degrees (100 to 150 degrees typical)
Classes of amplifiers
class A
class B
class AB
class C

## Slide 4: Class A and class B amplifiers
Class A output stage is a simple linear amplifier.
It is also very inefficient, typical maximum efficiency is between 10 and 20 %.
Only suitable for low power applications.
A class B output stage can be far more efficient than a class A stage (78.5 % maximum efficiency compared with 25 %).
It also requires twice as many output transistors…
…and it isn’t very linear; cross-over distortion can be significant.

## Slide 5: Class B amplifiers
When the dc base voltage is zero, both transistors are off and the input signal voltage must exceed VBE before a transistor conducts.
Because of this, there is a time interval between the positive and negative alternations of the input when neither transistor is conducting.
The resulting distortion in the output waveform is called crossover distortion.

## Slide 6
The DC collector current is NOT zero!
The DC collector current is lower than the peak amplitude of the ac collector current.
The DC collector current is very small, i.e., the Q point is close to the cut-off region.
Devices at the output stage conduct for more than 180 degrees (181 to 200 degrees typical).
Class AB amplifiers

## Slide 7: Push-pull: Class B vs Class AB
Class B
Class AB
Source
Sink
iL=iN (vi>0)
iL=iP (vi<0)
VBB≥1.4

## Slide 8: Class AB amplifier

## Slide 9: Circuit analysis & VTC
Devices are biased at a non-zero collector current!
DC analysis

## Slide 10: Circuit analysis & VTC
AC analysis

## Slide 11: Circuit analysis & VTC
AC analysis
L
KVL at loop L
Constant
base voltage
condition

## Slide 12: Circuit analysis & VTC

## Slide 13: Signal voltages and currents

## Slide 14: Voltage-transfer characteristic

## Slide 15: Output resistance
The output resistance is low. Great!

## Slide 16: Output resistance

## Slide 17: Efficiency

## Slide 18: Class AB amplifiers
A class AB output stage can be far more efficient than a class A stage (~40-65% maximum efficiency compared with 25 %) but less efficient than a class B stage (~40-65 % maximum efficiency compared with 78.5 %).
No cross-over distortion
Suitable for large signals
Intermediate characteristics between class A and B.

## Slide 19: Class AB amplifier
How can one practically realize the DC voltage VBB?

## Slide 20: Biasing of class AB amplifiers (push-pull AB)
Diode biasing
Biasing with VBE multiplier
Biasing with input buffer transistor

## Slide 21: Diode biasing
The biasing circuit comprising D1, D2, IBias, and V+ provides the biasing voltage VBB.
Current mirror
Diode connected transistors

## Slide 22: Diode biasing
As the input voltage increases, the output voltage increases, causing an increase in iCn. This in turn produces an increase in the base current iBn. Since the increase in base current is supplied by IBias, the current through D1 and D2, and hence the voltage VBB, decreases slightly.
Disadvantage:
VBB is not stable against variations of the output voltage.

## Slide 23: Diode biasing
As the temperature of the B-E junctions of the output devices increases, the biasing diodes that are in thermal contact with the emitter junctions will see an increase in temperature. As result the diode currents are going to increase and the base currents of the transistors are going to decrease, which leads to a decrease of the VBEn (VEBp) and of the iCn (iCp).
Benefit: prevents thermal runaway in the output devices if D1 and D2 are in thermal contact with them.

## Slide 24: Biasing using a VBE multiplier
Thus, VBB can be set by selecting suitable values for R1 and R2.
Neglecting the base current of Q1;
The biasing circuit comprising Q1, R1, R2 and IBias, provides the biasing voltage VBB.
Design parameters

## Slide 25: Biasing using a VBE multiplier
Bias is relatively stable against large variations of the output current.
As vI increases, iCn increases followed by an increase of iBn. iC1 decreases but vBE1 is almost constant.
It prevents thermal runaway in the output devices if Q1 is in thermal contact with them. (Why? Test your understanding trying to answer)

## Slide 26: Biasing using a VBE multiplier
To facilitate adjustment of the ratio R1/R2 and hence, the value of VBB, a third resistor Rv is typically included in the circuit.

## Slide 27: Biasing using buffer transistors
R1, R2 and the emitter-followers Q1 and Q2 establish the required quiescent bias.
The outputs of Q1 and Q2 follow the input signal and drive Q3 and Q4.
Benefits: stability and high current gain.

## Slide 28: Stability
When the input voltage vI increases, the base voltage of Q3 increases and the output voltage vO increases. The emitter current of Q3 increases to supply the load current iO.
The base current and the base voltage of of Q3 both increase. The increase in base voltage of Q3 reduces the voltage across, and the current through R1. This means that iB1 and iE1 also decrease and the vBE1 stays more or less constant.

## Slide 29: Current gain
Neglecting and
we have;
and;

## Slide 30: Current gain
If;
and;
then;

## Slide 31: Biasing using buffer transistors
Since the voltage gain is approximately unity, the output current is;
The current gain is;
which is quite substantial. A large current gain is desirable since the output stage must typically deliver large currents to a load

## Slide 32: In-class problem 1
A diode biasing class AB power amplifier is to meet the following specifications:
RL = 8 ;
Average output power delivered to the load PL = 5 W;
peak output voltage to be not more than 80% of VCC;
minimum value of ID to be no less than 5 mA

## Slide 33: In-class problem 1
For both Qn and Qp;
For D1 and D2
Determine;
a) IBias and VCC;
b) The quiescent collector current
c) iCn and iCp and VBB when the output voltage is at its peak positive value

## Slide 34: In-class problem 1, solution
a)
Select VCC = 12 V

## Slide 35: In-class problem 1, solution
At the positive peak of the output voltage;

## Slide 36: In-class problem 1, solution
To maintain a minimum of 5 mA through the diodes;
Select IBias = 20 mA

## Slide 37: In-class problem 1, solution
b)
Under quiescent condition (vI = 0), ID = 20 mA (neglecting iBn);

## Slide 38: In-class problem 1, solution
Assuming Qn and Qp are matched transistors;
Hence;

## Slide 39: In-class problem 1, solution
c)
At the peak positive value of output voltage;

## Slide 40: In-class problem 1, solution

## Slide 41: In-class problem 1, solution

## Slide 42: In-class problem 1, solution
Hence, when the output voltage is at its peak positive value;
and;

## Slide 43: Take-home problem 1
Determine the quiescent bias currents in all transistors;
Calculate all the currents labeled in the figure and the current gain when vI = 10 V.

## Slide 44: Take-home problem 1, solution
(a) For vI = 0 (quiescent currents);
Assuming all transistors are matched, the bias currents in Q3 and Q4 are also approximately 7.2 mA since the base-emitter voltages of Q1 and Q3 are equal and those of Q2 and Q4 are equal.

## Slide 45: Take-home problem 1, solution
(b) For vI = 10;
Because the voltage gain is approx. unity;

## Slide 46: Take-home problem 1, solution

## Slide 47: Take-home problem 1, solution
47
Since Q4 tends to turn off when vI increases, iB4 is negligible. Therefore;

## Slide 48: Take-home problem 1, solution
The input current;
The current gain;

## Slide 49: Take-home problem 1, solution
If the previous expression i.e.
we have;
is used,
The higher gain is due the fact that the base currents of Q3 and Q4 are neglected in deriving the expression.